## Slide 1
PPuTViOS 1
Programska podrška u televiziji i obradi slike
Laboratorijske vezbe – DTV platforma, SDK, IR, NIM, DMX
Zimski semestar školske godine 2017/2018
Notes: 1

## Slide 2
Uvod
Cilj predmeta: Upoznavanje sa hardverom i sofverom DTV prijemnika
Asistenti – kontakt na ime.prezime@rt-rk.com
  Dejan Nađ
  Sreten Tanacković
  Dušan Petković
  Goran Stupar
  Radovan Marković
  Nenad Lovčević
PPuTViOS1
2

## Slide 3
Organizacija lab vežbi
Pokazne vežbe + Individualni rad = Projekat
Pokazne vežbe
  DTV platforma + SDK + Remote Controller + DMX
  PSI/SI parsiranje + AV
  Rad sa grafikom – DirectFB
  Implementacija DTV aplikacije (zapper app) – osnova za početak projekta
Nakon svake pokazne vežbe dobija se rešenje
Nastavak kursa obavezne lab vežbe sa individualnim radom
PPuTViOS1
3

## Slide 4
Bodovanje
Prisustvo na pokaznim vežbama donosi 5 bodova
Prisustvo tokom izrade projekta ne donosi bodove ali je dolazak obavezan da bi se projekat završio blagovremeno
PPuTViOS1
4

## Slide 5
Radno okruženje
Host: Linux OS
Target: Linux OS
PPuTViOS1
5

## Slide 6
Mount (NFS)
NFS – Network File System – omogućava da na target uređaju “vidimo” direktorijum koji se nalazi na host mašini (i obrnuto)
Instaliranje NFS: (već urađeno na VM)
1.sudo apt-get install nfs-kernel-server
2.U /etc/exports na racunaru dodati sljedecu liniju na kraj <apsolutna putanja MOUNT_FOLDER-a> *(rw,no_root_squash,no_subtree_check
3. sudo service nfs-kernel-server restart
PPuTViOS1
6

## Slide 7
Telnet + Mount
Telnet – mrežni protokol za uspostavljanje dvosmerne komunikacije
Sa host mašine: telnet <ip_ploče>
Sa ploče: mount -o port=2049,nolock,proto=tcp -t nfs <ip_racunara>:<MOUNT_FOLDER putanja> /mnt/PPUTVIOS_Student1
PPuTViOS1
7

## Slide 8
Buildovanje
Izvorni kod se prevodi na host mašini a pokreće na target mašini tako da nam je potreban cross-compiler za target mašinu
Cross compiler se nalazi na putanji /home/student/pputvios1/toolchain/…
Skripta koja podesava putanju cross compilera je setenv_pputvios.sh
Pokretanje skripte za podešavanje putanja se izvršava sa source setenv_pputvios.sh
Source podešava promenljive koje važe SAMO važi samo sa sesiju terminala iz koje ste izvršili komandu (ako ugasite terminal, i upalite ga ponovo, morate ponovo da source-ujete)
Prevođenje izvornog koda: make
PPuTViOS1
8

## Slide 9
Pokretanje prevedenog koda
Da bi pokrenuli prevedeni kod, potrebno je da na ploči postoji “executable” tj prevedeni kod
Za to koristimo NFS tako što ćemo folder /home/student/pputvios1/ploca povezati sa /mnt/PPUTVIOS_StudentX -> mount
Sve što se na host računaru u direktorijumu nalazi u /home/student/pputvios/ploca nalaziće se na ploči u direktorijumu /mnt/PPUTVIOS_StudentX
Pokretanje programa se izvršava sa ./ime_programa
PPuTViOS1
9

## Slide 10
RC - Daljinski upravljač 1/2
IR prijemnik
int open(const char *pathname, int flags);
int ioctl(int fd, int request, ...);
ssize_t read(int fd, void *buf, size_t count);
PPuTViOS1
10

## Slide 11
RC - Daljinski upravljač 2/2
struct input_event {
struct timeval time;
unsigned short type;
unsigned short code;
unsigned int value;
};
type: EV_SYN (0), EV_KEY (1) , EV_REL(2) ...
value: relativna promjena za EV_REL , 0, 1 ili 2 za EV_KEY
PPuTViOS1
11

## Slide 12
Zadatak 1
Pokrenuti osnovni zadatak vezba_1.c
Analizirati ioctl funkciju
Analizirati getKeys funkciju
Proširiti osnovni zadatak tako da se čitanje pritisnutih tastera izvršava u posebnoj niti (koristiti pthread)
45 minuta, pa idemo dalje
Tips:
  pthreads https://computing.llnl.gov/tutorials/pthreads/
  Kreiranje niti - https://computing.llnl.gov/tutorials/pthreads/#CreatingThreads
  Joining - https://computing.llnl.gov/tutorials/pthreads/#Joining
  ioctl - http://man7.org/linux/man-pages/man2/ioctl.2.html
PPuTViOS1
12

## Slide 13
Zadatak 1 – Rešenje
Kopirati rešenje na nastavni_materijal i diskutovati
PPuTViOS1
13

## Slide 14: Hardver DTV prijemnika
Tuner
Demodulator
Demux
GPU
D/A sound convertor
Power supply
Flash memory
CPU
Video decoder
Audio decoder
D/A video convertor
I/O subsystem
PSI/SI
Video PES
Audio PES
OSD
Frames
Samples
Frames
Digital modulated TV signal
Front end
DVB Stream
Analog sound
Digital sound
Digital picture
Analog picture
Data

## Slide 15
TDP API - TunerDemuxPlayer
-Tuner -Player
Tuner_Init Player_Init
Tuner_Lock_To_Frequency Player_Deinit
Tuner_Register_Status_Callback Player_Source_Open
Tuner_Unregister_Status_Callback Player_Source_Close
Tuner_Get_Signal_Quality Player_Stream_Create
Tuner_Deinit Player_Stream_Remove
Player_Volume_Get
-Demux Player_Volume_Set
Demux_Set_Filter Demux_Register_Section_Filter_Callback
Demux_Unregister_Section_Filter_Callback
Demux_Free_Filter
PPuTViOS1
15

## Slide 16
TDP API
Dokumentacija: materijali\TDP_API\TDP_API.ppt
Domaći zadatak : materijali\TDP_API\tdp_api\tdp_api.h
TIP: kopirajte tdp_api direktorjium da možete da uradite domaći zadatak
PPuTViOS1
16

## Slide 17
Zadatak 2
Zadatak 2: Ispisati sadržaj PAT sekcije
Koraci:
  Izvršiti naredbu zaključavanja na frekvenciju XYZ
  Sačekati da se zaključavanje uspesno izvrši – callback
  Otvoriti „source“ - omogućiti tok podataka između tuner-a i demultipleksera
  Postaviti filter na demultiplekser za prijem PAT sekcija
  Ispisati sadržaj PAT sekcije
Tips:
  pthread_mutex_lock - https://computing.llnl.gov/tutorials/pthreads/#MutexCreation
  pthread_cond_timedwait - https://computing.llnl.gov/tutorials/pthreads/#ConditionVariables
  pthread_cond_signal- https://computing.llnl.gov/tutorials/pthreads/#ConditionVariables
PPuTViOS1
17

## Slide 18
Zadatak 2
Additional tips:
Timeval, timespec, gettimeofday(...)- http://www.tutorialspoint.com/unix_system_calls/settimeofday.htm
Ako timedwait ne radi, postavite I nanosekunde na nulu!
Obavezno 1: https://en.wikipedia.org/wiki/Callback_(computer_programming)
Obavezno 2: https://lmgtfy.com/?q=callback+implementation+in+c
PPuTViOS1
18

## Slide 19
Domaći zadatak
Ponoviti današnje vežbe i odgovoriti na sledeća pitanja
Šta je NFS i zašto radimo mount?
Šta je TELNET i zašto ga koristimo?
Šta je SDK i čemu služi?
Šta je to makefile, i zašto ga koristimo?
Na koji način smo očitavali pritisak na taster daljinskog upravljača?
Šta je to pthread, kako se kreira, kako se uništava, i kako radi?
Šta su to muteksi i conditional varijable?
Šta je tuner?
Šta je demultiplekser?
Šta je player?
Šta je callback?
PPuTViOS1
19

## Slide 20
Hvala na pažnji
Uradite vaš domaći zadatak